## Slide 1: How different biological signals are transduced
Module 279 18 B Medical Instrumentation I
Unit B 13.1 Measuring Biological Signals
Transducers
  Function
  Types
    capacitive
    photo-electric
    piezo-electric
    inductive
    pressure
    thermocouple
Electrodes
  Types
  Placement
  Electrode-electrolyte interface
  Application
13.1.1 Demonstrating how different biological signals are transduced
dr. Chris R. Mol, BME, NORTEC, 2015
©

## Slide 2: Physiological Signals:
Biological Signals
What is a Measurand?
A measurand is a physiological event that you want to measure ….
dr. Chris R. Mol, BME, NORTEC, 2015
What Measurands are there?
Position, motion, velocity acceleration, force, pressure, volume, flow, heat, temperature, humidity, light intensity, sound level, chemical composition, electric current, electric voltage, etc.
©

## Slide 3: Transducer Function
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
What is a Transducer?
A sensor is a transducer that converts the measurand (the thing you want to measure) into a signal that is compatible with a measurement system (often electrical).
An electrode is a sensor that directly acquires an electrical signal without the need to convert it to another form: both input and output are electrical signals.
Conversion of a physiological event into an electric signal makes it easier to use modern technology to process and display the event in a user-friendly format.
A transducer is any device used to convert energy from one form to another; typically when converting input energy into output energy.
An example is a microphone, which converts the input energy, the sound waves produced by a voice or instrument, to output energy, the electrical impulses in the form of amplified sound. Also: a loudspeaker which does the opposite.
What is an Electrode ?
What is a Sensor ?
©

## Slide 4: Transducer Types
Transducers
This presentation:
Capacitive transducers
Photo-electric transducers
Piezo-electric transducers
Inductive transducers
Pressure transducers
Thermo-couple transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Intermittent transducers give intermittent values (e.g. oral thermometer);
Continuous transducers give measurement values for a prolonged period of time
There are many more types of transducers, e.g. electrochemical, thermistors, radiation sensors, …
Direct transducers measure directly the measurand you are interested in.
Indirect transducers measure a derived value (e.g. Korotkoff sounds)
Invasive transducers need to be brought inside the body;
Non-invasive transducers work from the outside of the body.
Transducer characteristics:
©

## Slide 5: Capacitive Transducers
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
What is a Capacitive Transducer?
The capacitive transducer is a capacitor with variable capacitance. In the typical capacitor the distance between the two plates is fixed, but in variable capacitance transducers the distance between the two plates is variable.
What is it used for ?
It is used for the measurement of e.g. displacement (and related: velocity and acceleration) or pressure in many applications.
A capacitor can be constructed with two parallel plates separated by a non-conductive medium such as air. Capacitance depends on the area (A) of the plates and the distance (d) between the plates. The capacitance also changes with the dielectric constant (ε0) of the material used in it.
What is a Capacitance?
©

## Slide 6: Capacitive Transducers
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
How does it work ?
In the instruments using capacitive transducers the value of the capacitance changes due to change in the value of the input quantity that is to be measured (e.g. pressure, displacement).
This change in capacitance can be measured in an electronic circuit and can be calibrated against the input quantity. Thus the value of the input quantity can be measured directly.
©

## Slide 7: Capacitive Transducers: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Medical Applications: e.g. Invasive measurement of blood-pressure; intra-ocular pressure and intra-cranial pressure.
All at the tip of a catheter.
©

## Slide 8: Photo-electric Transducers
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
What is a
photo-electric sensor ?
This sensor uses the photo-electric effect to convert light energy into electrical energy. When light falls on photosensitive element, electric current is generated that is measured directly or after amplification.
It can be used to detect the distance, absence, or presence of an object.
What is the
photo-electric effect ?
This is the ejection of electrons of a metal or semi-conductor surface when illuminated by light (EM-radiation) of a suitable wave-length.
There are three different functional types:
  opposed (through beam),
  retro-reflective
  proximity-sensing (diffused)
©

## Slide 9: Photo-electric Transducers: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
These transducers are widely used in various medical applications, such as detectors for computed tomography (coupled with scintillators), instruments to analyse samples (immunoassay), and pulse oximeters.
Through beam application
in security
The Pulse oximeter measures oxygen concentration in blood via light transmission
The common solar cell used to generate electric solar power is a large area photodiode.
X-ray detection in CT scanning
©

## Slide 10: Piezo-electric Transducers
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
What is the
piezo-electric effect ?
Natural, single-crystal materials (gallium phosphate, quarts)
  have limited effect and long term stability.
Piezo-electric ceramics have higher sensitivity and are easier to shape.
What is a piezo-electric
transducer ?
What materials
show this effect?
The effect in some materials that electricity is generated when they are deformed or,
the other way around: when an electric current is applied, these materials are deformed.
Piezo- means 'press' or 'squeeze‘ (in Greek language)
A device that uses the piezoelectric effect, to measure changes in pressure, acceleration, temperature, strain, or force by converting them to an electrical charge.
©

## Slide 11: Piezo-electric Transducers: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
An early application of piezo transducer technology occurred during World War I with the use of sonar, which used echoes to detect the presence of enemy ships
A piezoelectric ultrasonic transducer generates ultrasonic activity, meaning it produces sound waves above the frequencies that can be heard by the human ear. It functions by rapidly expanding and contracting when appropriate electrical frequency and voltage is applied.
Piezoelectric transducers can be used for numerous applications for industrial, environmental and personal use. Air transducers, for instance, are frequently used in automobile, proximity and level sensors. They are commonly used in residential products like motion and object detectors, pest deterrents and home security alarms. They are also used in electronic devices, such as toys, games and remote control units. They are used in electronic sphygmo-mano-meters for measuring blood pressure and in phono-cardiography.
Ultrasound Imaging systems are used in various applications in hospitals to image unborn babies, heart valves, blood vessels, abdomens, etc. These are discussed in course: Medical Instruments II.
©

## Slide 12: Inductive Transducers
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
What is (magnetic)
induction?
What is an inductive
transducer?
Electromagnetic induction is the production of an electromotive force across a conductor when it is exposed to a time varying magnetic field.
Induction of the magnetic material depends on a number of variables like the number of turns of the coil on the material, the size of the magnetic material, and the permeability of the flux path.
Inductive transducers measure movement based on the fact that magnetic induction is changed by this motion. (The magnetic materials are used in the flux path and there are one or more air gaps. The change in the air gap results in change in the inductance of the circuit).
©

## Slide 13: Inductive Transducers: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Common applications of inductive sensors include metal detectors, traffic lights, car washes, etc. The sensor does not require physical contact, which makes it particularly useful for some applications.
Magneto EncephaloGraphy is a non-invasive technique for investigating human brain activity. It allows the measurement of ongoing brain activity on a millisecond-by-millisecond basis, and it shows where in the brain activity is produced.
The most sensitive low-field sensor is the superconducting quantum interference device (SQUID). SQUID magnetometers can detect fields from several femto-tesla up to 9 tesla, a range of more than 15 orders of magnitude. This is essential in medical applications since the neuro-magnetic field of the human brain is only a few tenths of a femto-Tesla; Earth's magnetic field, by way of comparison, is ~50 microTesla. SQUIDs require cooling to liquid helium temperature (4 kelvin) at present, but devices are under development that will operate at higher temperatures.
©

## Slide 14: Pressure Transducers
Transducers
What is a pressure
transducer/sensor
(manometer)?
dr. Chris R. Mol, BME, NORTEC, 2015
A pressure sensor measures pressure, typically of gases or liquids. Pressure is an expression of the force required to stop a fluid from expanding, and is stated in terms of force per unit area.
A pressure sensor usually generates an (electric) signal as a function of the pressure imposed.
Pressure sensors can vary drastically in technology, design, performance, application suitability and cost.
Technologies used can be e.g. capacitive, electro-magnetic, piezo-electric, optical, ….
A conservative estimate would be that there may be over 50 technologies and at least 300 companies making pressure sensors worldwide.
miniature fiber optic pressure sensor
©

## Slide 15: Pressure Transducers: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Pressure sensors are used for control and monitoring in thousands of everyday applications. Pressure sensors can also be used to indirectly measure other variables such as fluid/gas flow, speed, water level, and altitude.
Examples of Medical Applications:
  Invasive and non-invasive blood pressure monitors,
  fetal heart rate monitors
  Sleep apnea
  Flow meters (in ventilators)
©

## Slide 16: Thermo-Couples
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Any conductor that is subjected to a thermal gradient, will generate a voltage. This voltage depends on the material properties of the conductor.
What is the thermo-electric effect?
In a thermocouple, the thermo-electric effect is used to build a temperature-measuring device. It consists of two dissimilar conductors that contact each other at one or more spots, where a temperature differential is experienced by the different conductors (or semi-conductors).
The main limitation with thermocouples is their limited accuracy; system errors of less than one degree Celsius (°C) are difficult to achieve.
In contrast to most other methods of temperature measurement, thermocouples are self powered and require no external form of excitation.
What is a
thermo-couple?
©

## Slide 17: Thermo-Couples: applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Thermocouples are suitable for measuring over a large temperature range, from −270 up to 3000 °C Applications include temperature measurement for kilns, gas turbine exhaust, diesel engines, other industrial processes and fog machines.
They are less suitable for applications where smaller temperature differences need to be measured with high accuracy, for example the range 0–100 °C with 0.1 °C accuracy. For such applications thermistors, silicon bandgap temperature sensors and resistance thermometers are more suitable.
In medical applications body temperature is often an important parameter,
e.g. hypo-thermia in anaesthesia and in shock, for incubators, in arthritis, ….
©

## Slide 18: Electrodes
Transducers
Why is there electricity in the body?
Nerves send electric signals throughout the body to coordinate activities. Nerve (neuron) signals instruct muscles to contract, transport sense signals to the brain and signal a lot of data that we are not aware of. Also muscle activity is associated with electrical (biochemical) activity.
dr. Chris R. Mol, BME, NORTEC, 2015
What is the use of electrodes?
Yes, we can measure electric signal directly into nerves or nerve bundles and muscle cells. We can measure integrated activity from many nerves and muscles at the outside of the body, e.g. from the brain (EEG), the heart (ECG) and other muscles (EMG).
Can we measure this electricity?
Electrodes are electrical conductors which are positioned in the electro-magnetic field of the body. They register the electric signals of the body which can then be analysed and interpreted.
©

## Slide 19: Electrode Types
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Metal Plate Electrodes
  large surface electrodes for ECG
  metal disk electrodes for EMG, EEG
    stainless steel with coating of platinum or gold
  Disposable foam pad (cheap!) for ECG
Suction Electrodes
  no adhesives. For ECG (short term only)
application to limb
application with surgical tape
Floating Electrodes
  recessed metal disk (swimming in gel)
  less sensitive to motion
Flexible Electrodes (may fit better)
  polymer or nylon with silver deposits
  or carbon filled silicon rubber as thin film
©

## Slide 20: Electrode-electrolyte interface
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
The interface required for the charge transfer is the electrode – electrolyte interface.
The electrolyte is a conducting medium, specifically formulated for the electrode metal being used.
©

## Slide 21: Electrode Placement and Applications
Transducers
dr. Chris R. Mol, BME, NORTEC, 2015
Electrode placement in various clinical applications is further discussed elsewhere
ECG
EEG
Vector Cardiogram
EMG
©

## Slide 22
END
The creation of this presentation was supported by a grant from THET:
see https://www.thet.org/